This specification section uses numbered level paragraph styles which were not included in versions of Word prior to Word 97.  In the interests of clarity, all paragraph styles are formatted flush left.

Specification editor’s choice items are shown in [square brackets].  (Optional) paragraphs denote items available at additional cost.

Use TAB to go DOWN one paragraph number level; SHIFT+TAB to go one paragraph number level UP.

MOBILE STORAGE SHELVING UNITS  (Manually Operated BY spacesaver)

GENERAL

RELATED DOCUMENTS

Drawings and general provisions of the Contract, including General and Supplementary Conditions and Division 1 Specification Sections, apply to this Section.

SUMMARY

This Section includes the following:

Trolley mounted high-density mobile storage units, fabrication, and installation.

Related Work, Not Furnished:

Structural floor system capable of supporting live and dead loads required by prevailing building codes, including rolling loads of storage units to be installed.

Finish floor covering materials and installation

If optional photosweep and electric braking is to be included, retain the following paragraph.

Related Sections:

[Section 03300 – Concrete Work]

[Sections in Division 9 – Finishes, relating to finish floor and base materials.]

REFERENCES

Use the first reference paragraph only when cantilever shelves are specified.

American National Standards Institute (ANSI) Standards:

Applicable standards for fasteners used for assembly.

American Society for Testing and Materials (ASTM) Standards:

Applicable standards for steel materials used for fabrication.

American Institute Of Steel Construction (AISC) Standards:

      - Applicable standards for steel materials used for fabrication.

SYSTEM DESCRIPTION

General: The system consists of [manufactured][owner furnished] storage units mounted to manufacturer’s trolley system to form a compact storage system. System design permits access to any single aisle by manually moving units until the desired aisle is opened. The trolley system provides uniform carriage movement along the total length of travel.

Finishes:

Fabricated Metal Components And Assemblies: Manufacturer’s standard powder coat paint finish.

PERFORMANCE REQUIREMENTS

Design Requirements:

Limit overall height to [____] inches [____] MM.

Limit overall length to [____] inches [____] MM.

SUBMITTALS

Product Data: Submit manufacturer's product literature and installation instructions for trolley type high density mobile shelving.  Include data substantiating that products to be furnished comply with requirements of the contract documents.

Shop Drawings: Show fabrication, assembly, and installation details including descriptions of procedures and diagrams.  Show complete extent of installation layout including clearances, spacings, and relation to adjacent construction in plan, elevation, and sections. Indicate clear exit and access aisle widths; access to concealed components; assemblies, connections, attachments, reinforcement, and anchorage.

Show installation details at non-standard conditions. Furnish floor layouts, technical and installation manuals for every unit shipment with necessary dimensions for system configuration at the project site. Include installed weight, load criteria, furnished specialties, and accessories.

Provide layout, dimensions, and identification of each unit corresponding to sequence of installation and erection procedures.  Specifically include the following:

Location, position and configuration of pallet racking.

Plan layouts of positions of trolleys and shelving, including all required clearances.

Details of shelving, indicating method and configuration of installation on trolleys.

Provide location and details of anchorage devices to be embedded in or fastened to other construction.

Provide installation schedule and complete erection procedures to ensure proper installation.

Samples: Provide minimum 3 inch (76MM) square example of each color and texture on actual substrate for each component to remain exposed after installation.

Selection Samples: For initial selection of colors and textures, submit manufacturer's color charts consisting of actual product pieces, showing full range of colors and textures available.

Warranty:  Submit draft copy of proposed warranty for review by the [Architect] [Architect/Engineer] [Engineer] [Designer].

(Insert others as required)

Maintenance Data: Provide in form suitable for inclusion in maintenance manuals for mobile storage units. Data shall include operating and maintenance instructions, parts inventory listing, purchase source listing, emergency instructions, and related information.

Submit manufacturer's instructions for proper maintenance materials and procedures.

Submit manufacturer's printed instructions for maintenance of installed work, including methods and frequency recommended for maintaining optimum condition under anticipated use conditions. Include precautions against using materials and methods which may be detrimental to finishes and performance.

[Reference List: Provide a list of recently installed mobile storage units to be visited by owner, architect, and contractor. Intent of list is to aid in verifying the suitability of manufacturer's products and comparison with materials and product specified in this section.]

<Question the inclusion of the above paragraph in a technical specification section; it really belongs  in bidding qualification requirements.  It would be O.K. to leave it in on the chance that a writer not under control of Spacesaver might leave it out of their bidding requirements..>

QUALITY ASSURANCE

Manufacturer Qualifications: Engage an experienced manufacturer who is ISO 9001 certified for the design, production, installation and service of trolley mounted high-density mobile storage units.  Furnish certificate attesting manufacturer’s ISO 9001 quality system registration.

Installer Qualifications: Engage an experienced installer who is a manufacturer's authorized representative for the specified products for installing carriages and anchoring shelving units to carriages.

Minimum Qualifications: 1-year experience installing systems of comparable size and complexity to specified project requirements.

Guaranteed 24-hour service response time.

DELIVERY, STORAGE AND HANDLING

Follow manufacturer’s instructions and recommendations for delivery, storage and handling requirements.

PROJECT CONDITIONS

Field Measurements: Verify dimensions before fabrication. Indicate verified measurements on Shop Drawings.  Coordinate fabrication and delivery to ensure no delay in progress of the Work.

Established Dimensions: Where field measurements cannot be made without delaying the Work, establish dimensions and proceed with fabricating mobile storage units.  Coordinate construction to ensure actual dimensions correspond to established dimensions.

SEQUENCING AND SCHEDULING

Sequencing: Coordinate storage shelving system installation with other work to minimize possibility of damage and soiling during remainder of construction period.

Scheduling: Plan installation to commence after finishing operations, including painting have been completed.

Built-In Items: Provide components which must be built in at a time which causes no delays general progress of the Work.

Pre-installation Conference: Schedule and conduct conference on project site to review methods and procedures for installing mobile storage units including, but not limited to, the following:

Review project conditions and levelness of flooring and other preparatory work performed under other contracts.

Review and verify structural loading limitations.

Recommended attendees include:

Owner's Representative.

Prime Contractor or representative.

The [Architect] [Architect/Engineer] [Engineer/Architect] [Engineer] [Designer].

Manufacturer's representative.

Subcontractors or installers whose work may affect, or be affected by, the work of this section.

Warranty

Provide a written warranty, executed by Contractor, Installer, and Manufacturer, agreeing to repair or replace units which fail in materials or workmanship within the established warranty period.  This warranty shall be in addition to, and not a limitation of, other rights the Owner may have under General Conditions provisions of the Contract Documents.

All equipment not installed by a certified Spacesaver Installer shall be free from defects in materials and workmanship for sixty (60) days from the date of receipt of material.  During the 60-day warranty period, all parts are included at no cost.

All equipment shall be free from defects in materials and workmanship for one (1) year from the date of the customer’s written acceptance of installation when the product is installed by a certified Spacesaver Installer.  During the 1-year warranty period, all parts and labor are included at no cost.

[MAINTENANCE]

[Provide manufacturer’s extended maintenance agreement for [____] [years] [months], commencing on the day the standard maintenance warranty ends.]

PRODUCTS

MANUFACTURERS

General: Products are based upon mobile shelving system products manufactured by Spacesaver Corporation. Contingent on meeting specification requirements, other acceptable manufacturers may be included.

BASIC MATERIALS

General: Provide materials and quality of workmanship which meet or exceed established industry standards for products specified. Material thicknesses/gauges are manufacturer’s option unless indicated otherwise.

PALLET RACKING

- Welded Upright: Upright shall be a welded truss design. Upright frame posts shall be 14 gauge steel, box formed, 3” x 3” with teardrop notches located on 2” centers. Horizontal braces shall be 14 gauge steel, roll formed 1 ½” x 1 ½” channel welded to the upright frames. All welded upright frame construction shall meet AWS D1.3 certified welding standards.

- Beams: Beams shall be 14 gauge, 6” high beams.  Beam capacities are per pair of beams.  8’ long beams to have a capacity of 4,800 lbs.  10’ long beams to have a capacity of 4,200 lbs.  12’ long beams to have a capacity of 3,600 lbs.

- Uprights and beams to be powder coat painted black.

TROLLEY

- Trolleys shall be welded assemblies constructed of 8 gauge minimum steel with main structural face section 5” high. Provide each trolley with four load bearing wheels and four horizontal guide wheels. Trolley to include an adjustable wheel bracket.  One trolley to be used with each mobile shelving section.  Capacity to be 600 lbs. per trolley.

- Trolleys to be powder coat painted in choice of manufacturer’s standard colors.

WHEEL

- Wheels to be minimum 2.9” diameter with reinforced ribs at both sides of wheels to the outer rolling surface. Each wheel to have (2) shielded bearings and a load capacity rating of 330 pounds. Provide four load wheels and four horizontal guide wheels per trolley. Four per side.

WIRE DECKING

- Waterfall wire decking shall be1/4” diameter wire, fabricated on a 2 1/2” x 4” rectangular grid pattern with 1.5” front and rear formed flanges. Waterfall wire decking shall have three 16 gauge, 1 1/4” high steel structural reinforcements placed parallel along the depth of the decking and welded to the wire framing at each intersection.

LED LIGHT

- 4’ LED shop light. Quantity as noted.

HANDLE

- 5” minimum length closed loop handle

FOUR-POST SHELVING FOR LEVRACK MOBILE SHELVING

      - Design: Wedge-lock type consisting of uprights, shelves, and shelf supports, designed to be assembled without fasteners or clips. Shelves shall not have any holes on exposed surfaces. Front and back flanges shall be flush with outside faces of posts.  Design shall permit individual shelf adjustment and/or removal anywhere along the entire height of uprights.

      - Materials and Workmanship: Fabricate units from Class 1, cold-rolled steel sheet with all bends sharp and true and no exposed “knife” edges.

        - All units shall be free of burrs, sharp edges and projecting hardware with smooth, non-abrasive surfaces and edges.

        - After fabrication, shelving shall exhibit no dents, “oil canning”, buckling or other surface irregularities.

      - Uprights: Uprights shall consist of 18 gauge minimum cold rolled steel formed into a 1” wide “Angle” shape end post.  Keyhole-shaped slots are placed on 1 ½” centers vertically on the inner face of the posts.  “Closed” Angle uprights shall have a 24 gauge minimum closure panel between the posts, fully enclosing the full height and width of the shelving upright. Uprights to attach to moveable trolley.

      - Shelves: Standard shelves shall be 9/16” in height and be formed of 22 gauge minimum cold rolled steel with flanges on all four sides.  Front and rear flanges shall also be turned “down” and “in”.  Shelves to be adjustable on 1 ½” centers vertically.  Shelves to be supported front and back by two “H” style heavy duty shelf supports of 14 gauge minimum, cold rolled steel. Height of shelf, including shelf supports, shall be 1 1/4”. “H” style heavy duty shelf reinforcements per manufacturers standard requirements.

      - Load Carrying Capabilities: Provide shelf units capable of supporting 40 pounds per lineal foot with maximum deflection of L/140. Shelves shall exhibit no permanent deflection under fully loaded conditions.

      - Each shelving section to have a capacity of 600 lbs.

      - Uprights attach to trolley with two 3/8” fasteners.

      - Shelving to be powder coat painted in choice of manufacturer’s standard colors.

      - See attached drawing for required number of shelving levels.

FABRICATION

General: Coordinate fabrication and delivery to ensure no delay in progress of the Work.

FINISHES

Paint Finish: Provide factory applied electrostatic powder coat paint.

EXECUTION

EXAMINATION

Examine floor surfaces with Installer present for compliance with requirements for installation tolerances and other conditions affecting performance of mobile storage units.

Verify that building structural system is adequate for installing mobile storage units at locations indicated on approved shop drawings.

Verify that intended installation locations of mobile storage units will not interfere with nor block established required exit paths or similar means of egress once units are installed.

Prepare written report, endorsed by Installer, listing conditions detrimental to proper performance of mobile storage units, once installed.

Proceed with installation only after unsatisfactory conditions have been corrected.

INSTALLATION

Pallet Racking, Trolley, and Shelving Installation:

General: Follow layout and details shown on approved shop drawings and manufacturer's printed installation instructions. Position units level, plumb; at proper location relative to adjoining units and related work.

Pallet racking:

Install pallet racking per manufacturers installation instructions.

Carriages:

Place movable trolleys on pallet rack beams. Ensure that all wheels track properly.

Shelving Units:

Permanently fasten shelving units to fixed and movable carriages with two, 3/8” vibration-proof fasteners.

Stabilize shelving units following manufacturer's written instructions. Reinforce shelving units to withstand the stress of movement where required and specified.

FIELD QUALITY CONTROL

Verify shelving unit alignment and plumb after installation. Correct if required following manufacturer’s instructions.

Remove components which are chipped, scratched, or otherwise damaged and which do not match adjoining work.  Replace with new matching units, installed as specified and in manner to eliminate evidence of replacement.

ADJUSTING

Adjust components and accessories to provide smoothly operating, visually acceptable installation.

CLEANING

Immediately upon completion of installation, clear components and surfaces.  Remove surplus materials, rubbish and debris resulting from installation upon completion of work and leave areas of installation in neat, clean condition.

DEMONSTRATION/TRAINING

Schedule and conduct demonstration of installed equipment and features with Owner's personnel.

Schedule and conduct maintenance training with Owner's maintenance personnel. Training session should include lecture and demonstration of all maintenance and repair procedures that end user personnel would normally perform.

PROTECTION

Protect system against damage during remainder of construction period.  Advise Owner of additional protection needed to ensure that system will be without damage or deterioration at time of substantial completion.

You could use pre-printed schedules and simply add them as last page.  Just keep 3.8 Paragraph and add subparagraph: “A. Equipment Schedules, See next page.” or similar wording.

# END OF SECTION